| Launch Vehicle Combination | Number of Launches | First/Last Launch |
| --- | --- | --- |
| Thor (SLV-2) + Agena A | 16 | 21-Jan-1959 / 13-Sep-1960 |
| Atlas (LV-3A) + Agena A | 4 | 26-Feb-1960 / 31-Jan-1961 |
| Total for Agena A | 20 | 21-Jan-1959 / 31-Jan-1961 |

Launch summary for Agena A

| Launch Vehicle Combination | Number of Launches | First/Last Launch |
| --- | --- | --- |
| Thor (SLV-2) + Agena B | 44* | 26-Oct-1960 / 28-Aug-1964 |
| Thrust-Augmented Thor (SLV-2A/C) + Agena B | 3* | 29-Jun-1963 / 15-May-1966 |
| Atlas (LV-3A) + Agena B | 28 | 12-Jul-1961 / 21-Mar-1965 |
| Atlas (SLV-3) + Agena B | 1 | 9-Jun-1966 |
| Total for Agena B | 76 | 26-Oct-1960 / 9-Jun-1966 |

Launch summary for Agena B

| Launch Vehicle Combination | Number of Launches | First/Last Launch |
| --- | --- | --- |
| Thor (SLV-2) + Agena D | 22* | 28-Jun-1962 / 31-May-1967 |
| Thrust-Augmented Thor (SLV-2A/C) + Agena D | 60* | 28-Feb-1963 / 17-Jan-1968 |
| LTTAT** (SLV-2G/H) + Agena D | 22* | 9-Aug-1966 / 16-Jul-71 |
| Thorad (SLV-2G/H) + Agena D | 21* | 18-May-1968 / 25-May-72 |
| Atlas (LV-3A) + Agena D | 15 | 12-Jul-1963 / 20-Jul-1965 |
| Atlas (SLV-3) + Agena D | 48 | 14-Aug-1964 / 5-Nov-1967 |
| Atlas (SLV-3A) + Agena D | 12 | 4-Mar-1968 / 7-Apr-1978 |
| Atlas F + Agena D | 1 | 27-Jun-1978 |
| Titan 3B å (SLV-5B) | 29 | 29-Jul-1966 / 23-Oct-1970 |
| Titan 23B åå | 2 | 21-Jan-1971 / 22-Apr-1971 |
| Titan 33B åå | 3 | 21-Mar-1971 / 21-Aug-1973 |
| Titan 24B åå | 23 | 12-Aug-1971 / 21-Aug-1973 |
| Titan 34B åå | 11 | 10-Mar-1975 / 12-Feb-1987 |
| Total for Agena D | 269 | 28-Jun-1962 / 12-Feb-1987 |

Launch summary for Agena D

Specifications of the Agena:

|  | Agena A | Agena B/D |
| --- | --- | --- |
| Length | 5.94 m (19.5 ft) | 7.56 m (24.8 ft) |
| Diameter | 1.52 m (5 ft) |
| Weight | 3850 kg (8500 lb) Fuel: 2945 kg (6500 lb) | 7160 kg (15800 lb) Fuel: 6115 kg (13500 lb) |
| Propulsion | Bell XLR81-BA-5 liquid-fuel rocket; 68.9 kN (15500 lb) for 120 s | Bell XLR81-BA-9 liquid-fuel rocket; 71.1 kN (16000 lb) for 240 s |